## Slide 1: IAmDrone Intelligent Ambulance Drone
Madan Puttaswamy - Drone TX
Mudhassar Ibrahim Sajath - Ambulance TX
Thirukumaran Rajkumar - Drone RX
Ymmen Goel - Ambulance RX

## Slide 2: PROBLEM
Ambulances play an important role in the health care department. However, ambulances face the challenge of not being able to deliver medical attention on time.
Primary causes for the delay are usually unexpected road traffic or poor road infrastructure.
One of the most important considerations in emergency treatment is response time.

## Slide 3: PROJECT DESCRIPTION
In the event of an emergency, an ambulance with a drone is dispatched to the particular location.
Drones are not affected by factors such as road infrastructure, traffic, etc. and can reach the victim much earlier.
The drone carries with itself a compact defibrillator, medication and CPR. It also has an inbuilt speaker and a video camera, whose feed can be monitored from the ambulance.
A medical personnel in the ambulance can then monitor the condition of the victim and guide a layperson next to the victim while they perform the required first aid until the ambulance arrives.

## Slide 4: SYSTEM ARCHITECTURE
5.8 GHz Channel
2.4 GHz Channel

## Slide 5
AMPLIFIER
LPF
BPF
ANTENNA
BPF
LO
MIXER
MIXER
CIRCULATOR
LNA
SIGNAL PROCESSING
WAVEFORM
GENERATOR
POWER AMPLIFIER
BPF
TRANSCEIVER MODULE

## Slide 6: DRONE SPECIFICATIONS
Parameters | Values
Name of the drone | DJI MATRICE 100
Maximum Flight Time (with full load) | 20 mins
Maximum Flight Time(w/o load) | 40 mins
Maximum Range | 5 Km
Maximum payload | 3600 g
Cost | $3300
GPS compatible | Yes
Weight of the drone | 1755 g
Weight of the battery | 676 g
Total weight of the system | 6031 g
Battery Rating | 11,000mAh at 11.1 V

## Slide 7: ANTENNA
  The location of the victim is fixed but the position of the ambulance changes.
  The high gain omni directional antenna is used at the ambulance side to transmit the signal power to long distance.
  The antenna at the drone must be small in size and weight in order to lower the payload and it must be omnidirectional to receive signal from all direction.

## Slide 8: DRONE ANTENNA
PARAMETERS | VALUE
Model | Cisco E2100L
Frequency Range | Dual Band (2.4 &5.8 GHz)
Gain | 6 dBi
Radiation Pattern | Omnidirectional
Price | $8.50

## Slide 9: AMBULANCE ANTENNA
PARAMETERS | VALUE
Model | Ubiquiti AMO-2G13
Freq Range | 2.35 - 2.55 GHz
Gain | 13 dBi
Radiation Pattern | Omnidirectional
Cost | $245

## Slide 10: 2.4 GHz Communication Transmitter

## Slide 11: 2.4 GHz TRANSMITTER SYSTEM DIAGRAM

## Slide 12: CASCADED GAIN

## Slide 13: CASCADED NODE POWER

## Slide 14: CASCADED GAIN - YIELD ANALYSIS
** Yield Analysis for 1000 iterations. Min. Gain = 2.45dB and Max. Gain = 25.44 dB

## Slide 15: CASCADED NODE POWER – YIELD ANALYSIS
** Yield Analysis for 1000 iterations. Min. Node Power = 3.5dB and Max. Node Power = 26.54dB

## Slide 16: Components @ 2.4 GHz

## Slide 17: LOCAL OSCILLATOR
PARAMETER | SPECIFICATION
Manufacturer | Linear Technology
Model Number | LTC6945
Power | -6 to +3 dBm
Frequency Range | 0.35GHz to 6 GHz

## Slide 18: LOW PASS FILTER
PARAMETER | SPECIFICATION
Manufacturer | Crystek Corporation
Model number | CLPFL-0500
Insertion Loss | 2.8 dB(Nominal)
Frequency Range | DC to 500 MHz

## Slide 19: MIXER
PARAMETER | SPECIFICATION
Manufacturer | Linear Technology
Model Number | LT5579
Conversion Gain | 1.3 dB
P1dB(output) | 10 dBm
Output 3rd Order Intercept | 27.3 dBm
Frequency Range | 1.5 – 3.8 GHz

## Slide 20: BAND PASS FILTER
PARAMETER | SPECIFICATION
Manufacturer | Johanson Technology, Inc.
Model Number | 1810BP07B200T
Insertion Loss | 2 dB(Nominal)
Frequency Range | 1.4 – 2.6 GHz

## Slide 21
PARAMETER | VALUE
Model | SKY65006-348LF
Frequency | 1.5-3.5 GHz
Low Voltage Positive Bias supply | 3.3V
Low quiescent current | 50mA
Small Signal Gain | 40 dB
P1dB point | 37 dBm
POWER AMPLIFIER

## Slide 22
Pt = 21.22 dBm = 1 dBm
Transmitter Antenna gain, Gt = 6 dB = 21.22 dBm
Receiver Antenna gain, = 13 dB =(3.3*50m+5V*40mA+3.3V*226mA)W
EIRP = Pt * Gt =1110.8mW
After calculating,
EIRP = 27.22 dBm
After calculating,
PAE = 11.81%
f = 2.4 GHz
c = 3*108 m/s
= MDS = -75 dBm (SNR included)
Range = 5.7 Km

## Slide 23: 5.8 GHz Communication Receiver

## Slide 24: 5.8 GHz RECEIVER SYSTEM DIAGRAM

## Slide 25: CASCADED NOISE FIGURE
The RX maintains a low NF of 1.921 dB.

## Slide 26: CASCADED NF – YIELD ANALYSIS
Cascaded NF varies from 1.145 dB to 8.232 dB.

## Slide 27: CASCADED GAIN
The Rx needs has a gain of 34.53 dB.

## Slide 28: CASCADED GAIN – YIELD ANALYSIS
Cascaded Gain stays within the limit of 16.97dB to 53.36dB.

## Slide 29: CASCADED IP3
The cascaded IP3 of the Drone Receiver is 38.75 dBm.

## Slide 30: CASCADED IP3 – YIELD ANALYSIS
The cascaded IP3 has large variation from 14.57dBm to 51.6dBm.

## Slide 31: Components @ 5.8 GHz

## Slide 32: CIRCULATOR
PARAMETERS | VALUE
Model | 3C40C-8
Isolation | 20 dB
Insertion Loss | 0.3 dB

## Slide 33
PARAMETERS | VALUE
Insertion Loss | 0.5 dB
Noise Figure | 0.5 dB
BW | 125 Mhz
Frequency | 5.8 GHz
BANDPASS FILTER

## Slide 34
PARAMETERS | VALUE
Model no. | MAAL-011078
Gain | 23 dB
Noise Figure | 0.6 dB
P1dB | 17 dBm
OIP3 | 33 dBm
Vdc | 5 V
Idc | 50 mA
Freq Range | 700 – 6000 GHz
LNA

## Slide 35
PARAMETER | VALUE
Model no. | MR128
Loss | 5.5 dB
NF | 8 dB
Freq range | 4 – 18 (GHz)
Drive Level | 23 dBm
P1dB | 18dBm
IIP3 | 28 dBm
LO power(max) | 353 mW
DC Operation | 4.2V, 84mA
MIXER WITH LO

## Slide 36: LOW PASS FILTER
PARAMETERS | VALUE
Model | B73220M1
Insertion Loss | < 1.5 dB
Frequency Range | 113 - 269 MHz

## Slide 37: IF AMPLIFIER
PARAMETERS | VALUE
Model | LTC6420
Gain | 20 dB
Frequency Range | LF - 850 MHz
NF | 6.2 dB
OIP3 | 46 dBm
Pdc | 240 mW

## Slide 38: HAND CALCULATIONS
Pt = 11.28 dBm
Gain of Transmitter antenna = 13 dBi
Gain of the Receiver antenna = 6 dBi
EIRP = Pt * Gt = 24.28 dBm = 267.91 mW
f = 5.4 GHz Pin = -15 dBm, Pout = 19.42 dBm
C = 3x Pdc = (5V x 50mA) + (4.2V x 84 mA) + 240mW
MDS = -83 dBm PAE = 10.37 %
Rmax = 2.039 Km

## Slide 39: BATTERY
Lithium Polymer Battery
Specs: 11,000 mAh, 11.1 V
Price: $249.99
*Various voltage regulators and convertors will be used according to component requirements.

## Slide 40
PROP
PROPERTIES | SPECIFICATION | PROJECTED PERFORMANCE | COMPLIANT
Operating Frequency (GHz) | 2.4GHz-2.5GHz (Centre frequency 2.4 GHz) | 2.4GHz-2.45GHz (Centre frequency 2.4 GHz) | Yes
Transmitted Power | 20 dBm | 21.22 dBm | Yes
Noise Figure (RX) | 12 dB | 3.495 dB | Yes
Maximum Range | 5 km | 5.7 Km | Yes
Minimum Detectable Signal | -80 dBm | -75 dBm | Yes
Maximum Antenna Gain(dBi) | 12 dBi | 13 dBi | Yes
DC Power (Ambulance) | 10W | 4.5W | Yes
COMPLIANCE MATRIX FOR 2.4GHz CHANNEL

## Slide 41: COMPLIANCE MATRIX FOR 5.8GHz CHANNEL
PROPERTIES | SPECIFICATION | PROJECTED PERFORMANCE | COMPLIANT
Operating Frequency (GHz) | 5.725 – 5.85 GHz fc = 5.8 GHz | 5.725 – 5.85 GHz fc = 5.8 GHz | YES
Transmitted Power ( max allowed ) | 24 dBm | 24.28 dBm | ALLOWABLE
Noise Figure (RX) | 12 dB | 1.912 dB | YES
Maximum Range | 5 Km | 2.039 Km | NO
Minimum Detectable Signal | -87 dBm | -83 dBm | YES
Maximum Antenna Gain (Rx dBi) | 7 dBi | 6 dBi | ALLOWABLE
Expected DC power (TX and Rx Drone) | 2 W | 1.94W | YES

## Slide 42: FINANCIAL ANALYSIS
COMPONENT | COST (Approx.)
Drone | $3300
Ambulance Transceiver | $360 + $320
Drone Transceiver | $550 + $2100
Miscellaneous (signal processor and on-Board Radar) | $1500
Total | $8130
The total cost of the product is acceptable if its application in the ambulance taken into consideration.

## Slide 43: MILESTONES
Activity/Time Period | Sep | Oct | Nov | Dec | Jan | Feb | March
Analyzing the issues of design |  |  |  |  |  |  | 
System level design |  |  |  |  |  |  | 
Software implementation |  |  |  |  |  |  | 
Testing and debugging |  |  |  |  |  |  | 
Fabrication of the system and implementation |  |  |  |  |  |  | 
Transceiver module testing |  |  |  |  |  |  | 
Final implementation with the drone |  |  |  |  |  |  | 

## Slide 44: PERFORMANCE / PROPAGATION ISSUES
  The Drone covers only 2 Km against 5 Km due to limitation of low mAH Battery and high payload.
  Desired signal must be strong enough to be not affected by blocker frequencies.
  Transceiver’s placement at drone had to be adjusted so that it does not affect its flight.
  The Sensitivity of the receiver must be strong enough to detect the appropriate signal from the unwanted signals.

## Slide 45: MANUFACTURING AND TEST ISSUES
  As failure of the system can cost a life, Kaizen and six sigma process is employed to ensure not more than (3.4 defects per million).
  A real life scenario with many ISM band devices is simulated to test the performance of Transceiver.
  The Drone is attached to Defibrillator which increases its payload.

## Slide 46
  Health Issues :
    The Maximum Permissible Exposure level set by IEEE is 2mW @ 2.4GHz and 4mW @ 5.8 GHz. The power transmitted in the form of radiation in the system is lower than the MPE.
    Environmental Issues :
Components chosen for the system are compliant to RoHS (Restriction of Hazardous Substances) to save environment.
HEALTH & ENVIRONMENT ISSUES

## Slide 47: CONSUMER ISSUES
    There is a possibility, albeit very low of the drones colliding with people or other objects.
    The drones will be registered with the Federal Aviation Administration of the United States.

## Slide 48: Thank You

## Slide 49: APPENDIX

## Slide 50: 2.4 GHz RECEIVER SYSTEM DIAGRAM

## Slide 51: CASCADED NOISE FIGURE
The RX maintains a low NF of 3.5dB.

## Slide 52: CASCADED NOISE FIGURE - YIELD ANALYSIS
Cascaded NF does not vary much. Range is 2.8 dB to 4.8 dB.

## Slide 53: CASCADED GAIN
The Rx needs a high gain of 54 dB.

## Slide 54: CASCADED GAIN - YIELD ANALYSIS
Cascaded Gain stays within the limit of 45dB to 56dB.

## Slide 55: CASCADED IP3 - YIELD ANALYSIS
The cascaded IP3 has large variation from 10dBm to 37 dBm.

## Slide 56: CIRCULATOR
PARAMETERS | VALUE
Model | SX-10WR
Isolation | 20 dB
Insertion Loss | 0.5 dB

## Slide 57
PARAMETERS | VALUE
Insertion Loss | 1 dB
Noise Figure | 1 dB
BW | 100 Mhz
Frequency | 2.4 GHz
BANDPASS FILTER

## Slide 58
PARAMETERS | VALUE
Model no. | BGU7224
Gain | 25
Noise Figure | 1.5 dB
P1dB | 22 dBm
OIP3 | 32 dBm
Vdc | 10V V
Idc | 110mA
Freq Range | 2.4 – 2.5 GHz
LNA

## Slide 59
PARAMETER | VALUE
Model no. | ML485
Loss | 8.5 dB
NF | 11 dB
Freq range | 1.5-3.2 (GHz)
Drive Level | 0 dBm
P1dB | 11dBm
IIP3 | 37 dBm
LO power(max) | 10dBm
DC Operation | 7V,40mA
MIXER WITH LO

## Slide 60: LOW PASS FILTER
PARAMETERS | VALUE
Model | BLP-150
Insertion Loss | 1 dB
Frequency Range | 150 MHz

## Slide 61: IF AMPLIFIER
PARAMETERS | VALUE
Model | BGA7351
Gain | 22 dB
Frequency Range | 50-500 MHz
P1dB | 16.5 dBm
OIP3 | 46 dBm
Vdc,Idc | 5 V, 3 mA

## Slide 62: HAND CALCULATIONS
Pt = 21.22 dBm = -39 dBm
Transmitter Antenna gain, Gt = 6 dB = 16.5 dBm
Receiver Antenna gain, = 13 dB = 10*110+7*40+5*3*2 mW
EIRP = Pt * Gt = 1.5 W
After calculating,
EIRP = 27.22 dBm (527.22 mW)
After calculating,
PAE = 3.2%
f = 2.4 GHz
c = 3*108 m/s
= MDS = -75 dBm (SNR included)
Range = 5.7 Km

## Slide 63
PROP
PROPERTIES | SPECIFICATION | PROJECTED PERFORMANCE | COMPLIANT
Operating Frequency (GHz) | 2.4GHz-2.45GHz (Centre frequency 2.4 GHz) | 2.35GHz-2.45GHz (Centre frequency 2.4 GHz) | Yes
Transmitted Power | 20 dBm | 21.22 dBm | Yes
Noise Figure (RX) | 12 dB | 3.495 dB | Yes
Maximum Range | 5 km | 5.7 Km | Yes
Minimum Detectable Signal | -80 dBm | -75 dBm | Yes
Maximum Antenna Gain(dBi) | 12 dBi | 13 dBi | Yes
COMPLIANCE MATRIC FOR 2.4GHz CHANNEL

## Slide 64
5.8 GHz TRANSMITTER SYSTEM DIAGRAM

## Slide 65: CASCADED GAIN

## Slide 66: CASCADED GAIN - YIELD ANALYSIS
Cascaded Gain varies between 13.74dB to 28.99dB.

## Slide 67: CASCADED NODE POWER
The cascaded Node Power of the Ambulance Transmitter is 39.73 dBm.

## Slide 68: CASCADED NODE POWER - YIELD ANALYSIS
The cascaded node power fluctuates between 3.115dBm to 19.06dBm.

## Slide 69: TX ANTENNA
PARAMETERS | VALUE
Model | AIR-ANT2422DB-R-OEM
Gain | 2.2 dBi
Radiation Pattern | Omnidirectional
Cost | $245

## Slide 70
PARAMETERS | VALUE
Manufacturer | Teletronics
Model | 17-202
Insertion Loss | 3 dB
Noise Figure | 0.5 dB
BW | 150 Mhz
Frequency | 5.8 GHz
BANDPASS FILTER

## Slide 71
PARAMETERS | VALUE
Model no. | HMC599ST89
Gain | 14.5 dB
Noise Figure | 2.2 dB
P1dB | 19 dBm
OIP3 | 39 dBm
Vdc | 5 V
Idc | 120 mA
Freq Range | 50 – 1000 MHz
LNA

## Slide 72
PARAMETER | VALUE
Model no. | HMC787A
Loss | 9 dB
NF | 9 dB
Freq range | 3 – 10 (GHz)
Drive Level | 17 dBm
P1dB | 17dBm
IIP3 | 24 dBm
MIXER

## Slide 73: POWER AMPLIFIER
PARAMETERS | VALUE
Model | HMC659LC5
Gain | 19 dB
Frequency Range | DC - 15 GHz
NF | 3 dB
OIP3 | 35 dBm
Vdc | 8V
Idc | 300mA

## Slide 74
PARAMETERS | VALUE
Model | HMC431LP4
Frequency Range | 5.5 - 6.1 GHz
Output Power | 2 dBm
Supply Voltage | 3V
Supply Current | 27mA
LOCAL OSCILLATOR

## Slide 75: HAND CALCULATIONS
Pt = 11.28 dBm
Gain of Transmitter antenna = 13 dBi
Gain of the Receiver antenna = 6 dBi
Pin = -10 dBm, Pout = 11.28 dBm
Pdc = (3V*27mA) + (5V*120mA) + (8V*300mA)= 3081mW
PAE = 1.66 %
Rmax = 2.039 Km

## Slide 76: COMPLIANCE MATRIC FOR 5.8GHz CHANNEL
PROPERTIES | SPECIFICATION | PROJECTED PERFORMANCE | COMPLIANT
Operating Frequency (GHz) | 5.725 – 5.85 GHz fc = 5.8 GHz | 5.725 – 5.85 GHz fc = 5.8 GHz | YES
Transmitted Power ( max allowed ) | 24 dBm | 24.28 dBm | ALLOWABLE
Noise Figure (RX) | 12 dB | 1.912 dB | YES
Maximum Range | 5 Km | 2.039 Km | NO
Minimum Detectable Signal | -83 dBm | -83 dBm | YES
Maximum Antenna Gain (Rx dBi) | 7 dBi | 6 dBi | ALLOWABLE
Expected DC power (TX and Rx Drone ) | 2 W | 1.2W | YES